## Slide 1: TPL Algorithm
A Thermal Based Placement Algorithm

## Slide 2: Contents
Designs
Data Structures
Thermal Placement Algorithm

## Slide 3: Program Diagram
algorithm
data
structure
Parsers
net
force
target
move
force
target
Generators

## Slide 4: 1. Parsers
Read and write .nodes, .net and .pl files
NodesParser
PlParser
NetParser
Implemented using Boost.Spirit
In-memory Database design
  Use Circuit related data structure
  Use algorithm friendly counterpart

## Slide 5: 1. Parsers - Nodeparser
BookshelfNode
  Id id // typedef std::string Id
  int width
  int height
  bool fixed
  BookshelfNodes
    int num_nodes // total modules
    int terminals // fixed modules
    vector<BookshelfNode> data

## Slide 6: 1. Parsers - Plparser
BooshelfPl
  Id id
  Coordinate x // typedef double Coordinate
  Coordinate y
  bool fixed
  BookshelfPls
    vector<BookshelfPl> data

## Slide 7: 1. Parsers - Netparser
BooshelfPin
  Id id
  IOtype io // enum IOtype {Input, Output}
  Distance dx //shift of the pin from the center of the module
  Distance dy
  BookshelfNet
    Id id
    unsigned int degree // number of pins attached on this net
    vector<BookshelfPin> data
  BookshelfNets
    unsigned int num_nets // total nets
    unsigned int num_pins // total pins
    vector<BookshelfNet> data

## Slide 8: 2.Circuit Related Data Structures
TplModule
  Block
  Ternimal
from .nodes and .pl file to x,y coordinates and widths and heights
TplModules
  double chipwidth, chipheight
  size_t _num_modules, _num_free
  vector<TplModule> _modules
  functions operating _modules // etc. [ ], at, begin()

## Slide 9: 2.Circuit Related Data Structures
TplDB
  constructors
  static TplDB *instance // singleton pattern
  read_file()
  initialize_modules() // construct TplModules using BookshelfNodes & BookshelfPls
  initialize_nets() // construct TPlNets using BookshelfNets

## Slide 10: 3. netforce placement algorithm
TplNetForceModelInterface
  //
  compute_net_force_weight()
    iterate over TplNets, calculate weight of every two-pin pair in a net
    if p and q are inner pins, else 0
  compute_net_force_target()
    compute target destination by net force
    use Eigen::SimplicialLLT

## Slide 11: 3. netforce placement algorithm
TplNetForceModelInterface
  //
  compute_net_force_matrix() // compute matrix C and d
    if module[i] and module[j] are movable:
      C[i, i], C[j, j] += weight
      C[i, j], C[j, i] -= weight
      d[i] += weight * (pin[i] – pin[j])
      d[j] += weight * (pin[j] – pin[i])
    else if module[i] is fixed and module[j] is movable:
      C[j, j] += weight
      d[j] += weight * (pin[j] – pin[i] – module[i])
    else if module[i] is movable and module[j] is fixed:
      same as previous
    else: continue

## Slide 12: 4. Thermal Placement Algorithm
TplMoveForceModelInterface
  green_function() // return temperature at grid[i, j] calculated by approximate green function
  power_density() // return power density at grid[i, j] considering mirror symmetry
  update_green_function() // calculate
  update_power_density() // calculate

## Slide 13: 4. Thermal Placement Algorithm
Problem in TplMoveForceM
  update_green_function = , n = grid_size
  grid_size | chip_width / grid_size <= min{module_width}
  grid_size | chip_height / grid_size <= min{module_height}
  need to make this function faster

## Slide 14: Global Placement Diagram
When to re-partition into grids?
Hold force := - net force
Now we don’t have a given net

## Slide 15
Modules distribution
Partition into grids
Extend chip to nine regions

## Slide 16
Modules distribution
Thermal distribution
For each grid(i, j), calculate
where
and g[i, j] is the average power density of all blocks in the grid, that is each block’s power density multiplied by the portion of that block in the grid

## Slide 17
Thermal distribution
Heat flux
For each grid(i, j), calculate
This is the heat vector in every grid. To get the heat vector for each block, we add the heat vector of all grids that this block covers(need further discuss)
Heat flux
Quadratic optimization