## Slide 1: TPL Algorithm
A Thermal Based Placement Algorithm

## Slide 2: Contents
Designs
Data Structures
Thermal Placement Algorithm

## Slide 3: Program Diagram
algorithm
data
structure
Parsers
net
force
target
move
force
target
Generators

## Slide 4: 1. Parsers
Read and write .nodes, .net and .pl files
NodesParser
PlParser
NetParser
Implemented using Boost.Spirit
In-memory Database design
  Use Circuit related data structure
  Use algorithm friendly counterpart

## Slide 5: 2.Circuit Related Data Structures
TplModule
  from .nodes and .pl file to x,y coordinates and widths and heights
TplModules
  chipwidth, _num_free, _modules …
TplDB
  static TplDB *instance // singleton pattern
  read_file()
  initialize_modules() // BookshelfNodes & BookshelfPls
  initialize_nets() // BookshelfNets

## Slide 6: 3. netforce placement algorithm
TplNetForceModelInterface
  bound2bound model
  Kraftwerk2—A Fast Force-Directed Quadratic Placement Approach Using an Accurate Net Model

## Slide 7: 3. netforce placement algorithm
TplNetForceModelInterface
  compute_net_force_weight()
    iterate over TplNets, calculate weight of every two-pin pair in a net
    if p and q are inner pins, else 0

## Slide 8: 3. netforce placement algorithm
TplNetForceModelInterface
  compute_net_force_matrix()
    compute matrix C and d
    if module[i] and module[j] are movable:
      C[i, i], C[j, j] += weight
      C[i, j], C[j, i] -= weight
      d[i] += weight * (pin[i] – pin[j])
      d[j] += weight * (pin[j] – pin[i])
    else if module[i] is fixed and module[j] is movable:
      C[j, j] += weight
      d[j] += weight * (pin[j] – pin[i] – module[i])
    else if module[i] is movable and module[j] is fixed:
      same as previous
    else:
      continue

## Slide 9: 3. netforce placement algorithm
TplNetForceModelInterface
  compute_net_force_target()
    compute target destination by net force
    use Eigen::SimplicialLLT

## Slide 10
4. Thermal Placement Algorithm

## Slide 11
Modules distribution
Partition into grids
Extend chip to nine regions

## Slide 12
Modules distribution
Thermal distribution
For each grid(i, j), calculate
Ts[i, j] is the thermal signature at grid(i, j)
[i, j; ] is the approximate green function of grid(i, j) to grid()
and g[i, j] is the average power density of all blocks in the grid, that is each block’s power density multiplied by the portion of that block in the grid

## Slide 13
Thermal distribution
Heat flux
Heat flux
move force target
For each grid(i, j), calculate
This is the heat vector in every grid. To get the heat vector for each block, we add the heat vector of all grids that this block covers(need further discuss)

## Slide 14: 4. Thermal Placement Algorithm
TplMoveForceModelInterface
  green_function() // return temperature at grid[i, j] calculated by approximate green function
  power_density() // return power density at grid[i, j] considering mirror symmetry
  update_green_function() // calculate
  update_power_density() // calculate

## Slide 15: 4. Thermal Placement Algorithm
Problem in TplMoveForceM
  update_green_function = , n = grid_size
  grid_size | chip_width / grid_size <= min{module_width}
  grid_size | chip_height / grid_size <= min{module_height}
  need to make this function faster